## Slide 1: Hands-On Ethical Hacking and Network Defense, Edition 4
Module 11: Hacking Wireless Networks
Simpson, Antill, Wilson | Hands-On Ethical Hacking and Network Defense, 4th Edition. © 2023 Cengage. All Rights Reserved. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 2: Module Objectives
By the end of this module, you should be able to:
  Explain wireless technology
  Describe wireless networking standards
  Describe the process of authentication
  Describe wardriving
  Describe wireless hacking and tools used by hackers and security professionals

## Slide 3: Understanding Wireless Technology
For a wireless network to function, you must have:
  The right hardware and software
  Technology that sends and receives radio waves
Wireless technology is part of daily life
  Baby monitors
  Cell phones and smartphones
  Global positioning system (GPS) devices
  Keyless entry, remote controls, and garage door openers
  Two-way radios
  Bluetooth speakers

## Slide 4: Components of a Wireless Network (1 of 3)
Only a few basic components:
  Wireless network interface cards (WNICs)
    Transmit and receive wireless signals
  Access points (APs)
    The bridges between wired and wireless networks
  Wireless networking protocols
  A portion of the RF spectrum

## Slide 5: Components of a Wireless Network (2 of 3)
Access point (AP)
  Radio transceiver that connects to a network via an Ethernet cable
  Links a wireless LAN (WLAN) to a wired network
    Not all connect to a wired network
    Most companies use WLANs connected to the company’s wired network topology
  Point where RF channels are configured
  Enables users to connect to a LAN
    Using wireless technology
    Available only within a defined area

## Slide 6: Components of a Wireless Network (3 of 3)
Source: GNU General Public License (GNU GPL)
Figure 11-1 AP channels detected

## Slide 7: Service Set Identifiers (1 of 4)
SSID
  Name used to identify a WLAN
Configured on the AP
  Unique 1- to 32-character alphanumeric name
  Case-sensitive

## Slide 8: Service Set Identifiers (2 of 4)
To access the WLAN the AP connects to, wireless-enabled computers must configure with the same SSID as the AP
  The SSID name is attached to each packet to identify it as belonging to that wireless network
  AP usually broadcasts SSID several times a second
    Users with WNICs can see a display of all WLANs within range of the AP’s signal

## Slide 9: Service Set Identifiers (3 of 4)
Source: Microsoft Windows
Figure 11-2 SSIDs advertised to a Windows computer

## Slide 10: Service Set Identifiers (4 of 4)
Vendors
  Many have SSIDs set to a default value that companies never change
As a security professional, you must research constantly
  Wireless hackers can attempt to guess SSID
  Verify your clients are not using a default SSID
  A default SSID
    Tells an attacker that the target AP is out of date

## Slide 11: Configuring an Access Point (1 of 4)
Configuring an AP varies
  Depending on the embedded OS supplied by the manufacturer
  Users can access the software through a web browser
    Because the AP has an embedded OS supporting a web server
Accessing and reconfiguring a wireless router running dd-wrt:
  Enter the IP address in a web browser
  Provide the user logon name and password
  After a successful logon, click the Status tab
  Click the Wireless tab to display the Wireless Interface
  Click the Wireless Security tab to configure security

## Slide 12: Configuring an Access Point (2 of 4)
Source: GNU General Public License (GNU GPL)
Figure 11-3 Viewing status information in dd-wrt

## Slide 13: Configuring an Access Point (3 of 4)
Source: GNU General Public License (GNU GPL)
Figure 11-4 Basic wireless configuration in dd-wrt

## Slide 14: Configuring an Access Point (4 of 4)
Source: GNU General Public License (GNU GPL)
Figure 11-5 Configuring wireless security in dd-wrt

## Slide 15: Wireless NICs
For wireless technology to work, each node or computer must have a WNIC
  WNIC converts radio waves into digital signals the computer understands
There are many WNICs on the market
  Be careful deciding which one to purchase
  Some tools require certain specific brands

## Slide 16: Understanding Wireless Network Standards
Standard
  Set of rules formulated by an organization
Institute of Electrical and Electronics Engineers (IEEE)
  Has standards specifying maximum cable length in an Ethernet network
  Sets rules to follow for wireless networks
  Working groups (WGs) of the IEEE are formed to develop new standards
    IEEE Project 802: Developed to create LAN and WAN standards
  WG names are assigned numbers
    Example: 11 for the Wireless LAN group
    Letters denote approved projects
      Example: 802.11a or 802.11b

## Slide 17: The 802.11 Standard
The first wireless technology standard
Defined specifications for wireless connectivity as 1Mbps and 2Mbps in a LAN
Applied to the Physical layer of the OSI model
Carrier sense multiple access/collision avoidance (CSMA/CA) is used instead of CSMA/CD (collision detection, used in Ethernet)
  This is because radio signals can mix and cause a potential signal collision
Wireless LANs
  Don’t have an address associated with a physical location
    An addressable unit is called a station (STA)

## Slide 18: The Basic Architecture of 802.11 (1 of 5)
802.11 uses a basic service set (BSS) as its building block
  BSS
    Collection of devices that make up a WLAN
Basic service area (BSA)
  The coverage area an AP provides
A WLAN running in infrastructure mode
  Always has one or more APs
Ad-hoc network
  An independent WLAN without an AP

## Slide 19: The Basic Architecture of 802.11 (2 of 5)
As long as a station is within its BSA, it can communicate with other stations in the BSS
To connect two BSSs:
  802.11 requires a distribution system (DS) as an intermediate layer
    BSS 1 connects to the DS, which in turn connects to BSS 2
    Data moves between a BSS and the DS through the AP

## Slide 20: The Basic Architecture of 802.11 (3 of 5)
Source: Cengage
Figure 11-6 Connecting two wireless remote stations

## Slide 21: The Basic Architecture of 802.11 (4 of 5)
IEEE specifications
  Define the operating frequency range of 802.11
    United States: The range is 2.4 to 2.4835 GHz
Each frequency band contains channels
  A channel breaks up the band into smaller frequency ranges
  The 802.11 standard defines 11 channels in the 2.4 to 2.462 GHz range
    If channels overlap, interference could occur

## Slide 22: The Basic Architecture of 802.11 (5 of 5)
The length of a sound wave is measured from the peak of one wave to the next
  A sound wave’s amplitude (height) and frequency determine its volume and pitch
    Frequency
      Rate at which sound waves repeat
    Cycle
      Completion of a repeating pattern of sound waves
    Bands
      Different frequencies used by different technologies to transmit sound

## Slide 23: Frequency Bands
Frequency | Range | Wavelength
Extremely low frequency (E L F) | 3 to 30 Hz | 100,000 km to 10,000 km
Super low frequency (SLF) | 30 to 300 Hz | 10,000 km to 1000 km
Voice frequency (VF) or ultra-low frequency (ULF) | 300 Hz to 3 KHz | 1000 km to 100 km
Very low frequency (VLF) | 3 to 30 KHz | 100 km to 10 km
Low frequency (LF) | 30 to 300 KHz | 10 km to 1 km
Medium frequency (MF) | 300 KHz to 3 MHz | 1 km to 100 m
High frequency (HF) | 3 to 30 MHz | 100 m to 10 m
Very high frequency (VHF) | 30 to 300 MHz | 10 m to 1 m
Ultra high frequency (UHF) | 300 MHz to 3 GHz | 1 m to 10 cm
Super high frequency (SHF) | 3 to 30 GHz | 10 cm to 1 cm
Extremely high frequency (EHF) | 30 to 300 GHz | 1 cm to 1 mm

## Slide 24: An Overview of Wireless Technologies (1 of 2)
Infrared (IR) technology
  Restricted to a single room or line of sight
    Infrared light can’t be seen by the human eye
      Cannot penetrate walls, ceilings, or floors
Narrowband
  Uses microwave radio band frequencies to transmit data
  Commonly used in:
    Cordless phones
    Garage door openers

## Slide 25: An Overview of Wireless Technologies (2 of 2)
Spread spectrum
  To move over radio waves, data must be modulated on the carrier signal or channel
    Modulation
      Defines how data is placed on carrier signal
    Spread spectrum modulation
      Data is spread across a large-frequency bandwidth instead of traveling across just one frequency band
  Uses the following methods:
    Frequency-hopping spread spectrum (FHSS)
    Direct sequence spread spectrum (DSSS)
    Orthogonal frequency division multiplexing (OFDM)
    Orthogonal frequency division multiplexing Access (OFDMA)

## Slide 26: Additional IEEE 802.11 Projects (1 of 5)
802.11b (referred to as Wi-Fi)
  Operates in the 2.4 GHz band
  Throughput increased to 11 Mbps from the 1 or 2 Mbps of the original 802.11
  Allows for 11 separate channels to prevent overlapping signals
    Only three channels (1, 6, and 11) can be combined without overlapping and creating interference
  Introduced Wired Equivalent Privacy (WEP)

## Slide 27: Additional IEEE 802.11 Projects (2 of 5)
802.11a standard
  Has a different operating frequency range from 802.11 and 802.11b
  Operates in three distinct bands in the 5 GHz range
  Throughput increases to 54 Mbps
802.11g standard
  Operates in the 2.4 GHz range
  Because it uses a different modulation, it uses the OFDM method
    Increases the throughput to 54 Mbps

## Slide 28: Additional IEEE 802.11 Projects (3 of 5)
802.11i standard
  Introduced Wi-Fi Protected Access (WPA)
  Corrected many security vulnerabilities in 802.11b
  Most important standard for security professionals
802.11e standard
  Has improvements that address the problem of interference
    When interference is detected, signals can jump to another frequency more quickly
802.11n standard
  Operates in the same frequency and uses same encoding as 802.11g
  Uses multiple antennas and wider channels
    Increases the throughput to 600 Mbps

## Slide 29: Additional IEEE 802.11 Projects (4 of 5)
802.11ac standard
  Uses the 5 GHz band
  Allows for higher throughput (up to 1 gigabit per second)
802.11ad standard
  Dubbed “WiGig”
  Allows for transfer rates up to 7 gigabits per second over the 2.4 GHz, 5 GHz, and 60 GHz bands

## Slide 30: Additional IEEE 802.11 Projects (5 of 5)
802.11ah standard
  Targets lower energy consumption
  Creates extended-range Wi-Fi networks
802.11aj standard
  Known as the China Millimeter Wave
  Goal: Maintain backward compatibility with 802.11ad
  Technology uses the 45 GHz and 60 GHz spectrums uniquely available in China
The 802.11x standard
  Branded as Wi-Fi 6
  Replaces 802.11ac as the de facto wireless standard
  Wi-Fi 6 maxes out at 10 Gbps, uses less power, is more reliable in congested environments, and supports better security

## Slide 31: Additional IEEE 802 Standards (1 of 2)
802.15 standard
  Addresses networking devices in one person’s workspace
    Wireless personal area network (WPAN)
    Bluetooth is a common example
802.16 standard
  Covers wireless metropolitan area networks (M A Ns)
  Defines the Wireless M A N Air Interface for wireless M A Ns
  Addresses the limited distance available for 802.11b WLANs
  Worldwide Interoperability for Microwave Access (WiMAX)
    Most widely used implementation of wireless M A N technology

## Slide 32: Additional IEEE 802 Standards (2 of 2)
802.20 standard
  Another M A N standard
  Known as Mobile Broadband Wireless Access (MBWA)
  Addresses wireless M A Ns for mobile users
    Traveling in trains, subways, or cars at speeds up to 150 miles per hour
  iBurst
    Most common implementation of MBWA
    Used widely in Africa and Asia

## Slide 33: Summary of Approved Wireless Standards (1 of 2)
Standard | Frequency | Maximum rate | Modulation method
802.11 | 2.4 GHz | 1 or 2 Mbps | FHSS/DSSS
802.11a | 5 GHz | 54 Mbps | OFDM
802.11b | 2.4 GHz | 11 Mbps | DSSS
802.11g | 2.4 GHz | 54 Mbps | OFDM
802.11n | 2.4 GHz & 5 GHz | 600 Mbps | OFDM
802.11ac | 5 GHz | 1 Gbps | OFDM
802.11ad | 2.4 GHz, 5 GHz, & 60 GHz | 7 Gbps | OFDM
802.11ah | 900 MHz | 347 Mbps | OFDM
802.11aj | 45 GHz & 60 GHz | 15 Gbps | OFDM

## Slide 34: Summary of Approved Wireless Standards (2 of 2)
Standard | Frequency | Maximum rate | Modulation method
802.11ax | 2.4 GHz & 5 GHz | 10 Gbps | OFDMA
802.15 | 2.4 GHz | 2 Mbps | FHSS
802.16 (WiMAX) | 10 to 66 GHz | 120 Mbps | OFDM
802.20 (Mobile Wireless Access Working Group) | Below 3.5 GHz | 1 Mbps | OFDM
Bluetooth | 2.4 GHz | 24 Mbps | Gaussian frequency shift keying (GFSK)
HiperLAN/2 | 5 GHz | 54 Mbps | OFDM

## Slide 35: Understanding Authentication
Problem of unauthorized users accessing resources on a network
  A major concern for security professionals
  An organization that introduces wireless technology to the mix increases the potential for security problems

## Slide 36: The 802.1X Standard
Defines the process of authenticating and authorizing users on a network
Basic concepts
  Point-to-Point Protocol (PPP)
  Extensible Authentication Protocol (EAP)
  Wired Equivalent Privacy (WEP)
  Wi-Fi Protected Access (WPA)
  Wi-Fi Protected Setup (WPS)

## Slide 37: Point-to-Point Protocol (PPP)
Many ISPs use PPP
  To connect dial-up or DSL users
  PPP handles authentication by requiring a user to enter a valid username and password
  PPP verifies that users attempting to use the link are who they say they are

## Slide 38: Extensible Authentication Protocol (EAP) (1 of 4)
EAP is an enhancement to PPP
  Designed to allow a company to select its authentication method
Example:
  A company can use certificates or Kerberos authentication to authenticate a user connecting to an AP
  Certificate
    Record that authenticates network entities, such as server or client
    Contains X.509 information
      Identifies the owner, the certificate authority (CA), and the owner’s public key

## Slide 39: Extensible Authentication Protocol (EAP) (2 of 4)
Source: Microsoft Windows
Figure 11-7 Viewing information about an x.509 certificate

## Slide 40: Extensible Authentication Protocol (EAP) (3 of 4)
EAP methods to improve security on wireless network:
  Extensible Authentication Protocol-Transport Layer Security (EAP-TLS)
  Protected EAP (P E A P)
  Microsoft P E A P
802.1X uses the following components to function:
  Supplicant
  Authenticator
  Authentication server

## Slide 41: Extensible Authentication Protocol (EAP) (4 of 4)
Source: Cengage
Figure 11-8 A supplicant connecting to an AP and a RADIUS server

## Slide 42: Wired Equivalent Privacy (WEP)
Part of the 802.11b standard
Developed to encrypt data traversing a wireless network
WEP encryption is easily cracked
  Due to a flaw in its RC4 encryption algorithm
Works well for home users or small businesses when combined with the security of a Virtual Private Network (VPN)

## Slide 43: Wi-Fi Protected Access (1 of 2)
WPA, WPA2, and WPA3
  Specified in the 802.11i standard
  Replacement for WEP
Improves encryption by using Temporal Key Integrity Protocol (TKIP) enhancements
  TKIP’s four enhancements that address encryption vulnerabilities in WEP
    Message Integrity Check (M I C)
    Extended Initialization Vector (IV) with sequencing rules
    Per-packet key mixing
    Rekeying mechanism
    Authentication mechanism using 802.1X and EAP

## Slide 44: Wi-Fi Protected Access (2 of 2)
WPA3
  Released in January 2018
  Officially replaces WPA2 and provides improved security features
  For encryption:
    Uses AES-256 and SHA-384 in WPA3-Enterprise mode
    Mandates the use of CCMP-128 (AES-128 in CCM Mode) as the minimum encryption algorithm in WPA3-Personal mode
    Uses Simultaneous Authentication of Equals (SAE) exchange
      Results in a more secure initial key exchange
  Difficult for hackers to tap into a network using offline password-guessing attacks
  Susceptible to timing attacks during the handshake process
    Information gathered can be used for a password partitioning attack

## Slide 45: Wi-Fi Protected Setup (WPS)
WPS
  A wireless authentication standard created to allow users to add devices easily and securely to a wireless network
  Eliminates the need for a user to enter a passphrase
    User simply presses a button on the router
    The WPS-able device pairs with the router
Flaw discovered in 2011
  Allows an attacker to gain access to a network remotely without knowing the WPA2 password

## Slide 46: Knowledge Check Activity 11-1
Which IEEE standard defines authentication and authorization in wireless networks?
802.11
802.11a
802.11b
802.1X
Notes: Instructions:
Use the Knowledge Check questions to periodically pose a question to students during class to gauge how well they can recall the material that was presented.

## Slide 47: Knowledge Check Activity 11-1: Answer
Which IEEE standard defines authentication and authorization in wireless networks?
Answer: d. 802.1X
The 802.1X standard defines the process of authenticating and authorizing users on a network. This standard is especially useful for WLAN security when physical access control is more difficult to enforce than on wired LANs.

## Slide 48: Polling Activity 11-1
Which wireless encryption standard offers the best security?
WPA3
WEP
WPS
WPA
Notes: Instructions:
  1. Use this activity to solicit student opinions about concepts in the module or to play a game.
  2. Go to kahoot.com, or the platform of your preference, and log in or sign up.
  3. Create the challenge.
  4. Teacher Tip: Turn off the timer to prioritize accuracy or turn on the nickname generator to avoid inappropriate nicknames.
  5. Invite players by sharing the link or PIN.
  6. This can be done synchronously during class or asynchronously for review or homework.

## Slide 49: Polling Activity 11-1: Answer
Which wireless encryption standard offers the best security?
Answer: a. WPA3
WPA3 makes it more difficult for hackers to tap into a network using offline password-guessing attacks. WPA2 would allow hackers to capture data from your router and use this data to repeatedly attempt to guess your password, but with WPA3, one incorrect hacking attempt renders this data useless. WPA3 also improves security over public Wi-Fi networks.

## Slide 50: Knowledge Check Activity 11-2
What protocol was added to 802.11i to address WEP’s encryption vulnerability?
MIC
TKIP
TTL
EAP-TLS
Notes: Instructions:
Use the Knowledge Check questions to periodically pose a question to students during class to gauge how well they can recall the material that was presented.

## Slide 51: Knowledge Check Activity 11-2: Answer
What protocol was added to 802.11i to address WEP’s encryption vulnerability?
Answer: b. TKIP
Temporal Key Integrity Protocol (TKIP) was added to the 802.11i standard as WEP was known to have cryptographic weaknesses. WEP was replaced by Wi-Fi Protected Access (WPA).

## Slide 52: Understanding Wardriving
Hackers use wardriving
  Driving around with inexpensive hardware and software that enables them to detect unsecured APs
Wardriving is not illegal
  But using the network resources discovered with wardriving is illegal

## Slide 53: How It Works
An attacker or security tester drives around with the following equipment:
  A Wi-Fi capable smartphone or laptop and software that scans the areas for SSIDs
  WNIC
    Not all are compatible with scanning software
      Review the software requirements before purchasing the hardware
Antenna prices vary depending on the quality and the range that they can cover
Most scanning software identifies:
  The company’s SSID
  The security type enabled
  The signal strength

## Slide 54: Vistumbler (1 of 3)
Freeware tool written for Windows that enables WLAN detection using certain access points
  802.11a, 802.11b, 802.11g, 802.11n, and 802.11ac
Easy to install
Primarily designed to assist security testers in the following:
  Verify WLAN configuration
  Detect other wireless networks that might be interfering with a WLAN
  Detect unauthorized APs that might have been placed on a WLAN
Capable of connecting to a GPS
  Enables a security tester or hacker to map locations of all WLANs the software detects

## Slide 55: Vistumbler (2 of 3)
Source: GNU General Public License (GNU GPL)
Figure 11-9 Configuring GPS settings in the Vistumbler Settings dialog box

## Slide 56: Vistumbler (3 of 3)
When Vistumbler identifies an AP signal, it logs the following:
  The SSID
  The MAC address
  The manufacturer of the AP
  The channel on which the signal was heard
  The signal strength
  Whether encryption is enabled
Attackers can detect APs within a 350-foot radius
  With better antennas, they can locate APs a couple of miles away

## Slide 57: Kismet (1 of 2)
Product for conducting wardriving attacks
  Written by Mike Kershaw
  Runs on Linux, BSD UNIX, macOS, and Linux PDAs
A sniffer and an intrusion detection system (IDS)
  Can sniff 802.11b, 802.11a, 802.11g, 802.11n, 802.11ac, and 802.11ax traffic
Features:
  Wireshark- and Tcpdump-compatible data logging
  Compatible with AirSnort and AirCrack
  Network IP range detection
  Detection of hidden network SSIDs

## Slide 58: Kismet (2 of 2)
Features (continued):
  Graphical mapping of networks
  Client or server architecture that allows multiple clients to view a single Kismet server at the same time
  Manufacturer and model identification of APs and clients
  Detection of known default AP configurations
  XML output
  Supports for dozens of card types

## Slide 59: Polling Activity 11-2
What information can be gathered by wardriving? (Choose all that apply.)
SSIDs of wireless networks
Whether encryption is enabled
Whether SSL is enabled
Signal strength
Notes: Instructions:
  1. Use this activity to solicit student opinions about concepts in the module or to play a game.
  2. Go to kahoot.com, or the platform of your preference, and log in or sign up.
  3. Create the challenge.
  4. Teacher Tip: Turn off the timer to prioritize accuracy or turn on the nickname generator to avoid inappropriate nicknames.
  5. Invite players by sharing the link or PIN.
  6. This can be done synchronously during class or asynchronously for review or homework.

## Slide 60: Polling Activity 11-2: Answer
What information can be gathered by wardriving?
Answer: a., b., and d. SSIDs of wireless networks, whether encryption is enabled, and signal strength
In wardriving, most scanning software detects the company’s SSID, the type of security enabled, and the signal strength, indicating how close the access point (AP) is to the attacker.

## Slide 61: Discussion Activity 11-1
Discuss Temporal Key Integrity Protocol and identify which TKIP enhancement addresses the WEP vulnerability of forging packets.
Notes: Instructions:
Use the Discussion activity to encourage group conversation about a related topic of interest.

## Slide 62: Discussion Activity 11-1: Answer
Discuss Temporal Key Integrity Protocol and identify which TKIP enhancement addresses the WEP vulnerability of forging packets.
Answer: Message Integrity Check (MIC)
Explanation: Temporal Key Integrity Protocol (TKIP) is used by Wi-Fi Protected Access (WPA) to improve encryption. TKIP has four enhancements that address vulnerabilities in WEP. The vulnerability of forging packets is addressed by the Message Integrity Check (MIC) enhancement. MIC, pronounced M-I-C and also called Michael, is a cryptographic message integrity code. Its main purpose is to prevent forgeries, which are packets that attackers create to look like legitimate packets.

## Slide 63: Understanding Wireless Hacking
Hacking a wireless network
  Not much different from hacking a wired LAN
Techniques
  Port scanning
  Enumeration tools

## Slide 64: Tools of the Trade (1 of 4)
Equipment:
  Laptop computer
  WNIC
  Antenna
  Sniffers
Tools for cracking WEP or WPA keys:
  Aircrack-ng

## Slide 65: Tools of the Trade (2 of 4)
Aircrack-ng
  The tool most hackers use to access WEP-enabled WLANs
  Replaced AirSnort
  Has some useful add-ons
    GUI front-end called Fern WIFI Cracker

## Slide 66: Tools of the Trade (3 of 4)
Source: GNU General Public License (GNU GPL)
Figure 11-11 Fern WIFI Cracker interface

## Slide 67: Tools of the Trade (4 of 4)
Source: Hak5 LLC
Figure 11-12 WiFi Pineapple interface

## Slide 68: Countermeasures for Wireless Attacks (1 of 3)
Consider using anti-wardriving software
  Makes it more difficult for attackers to discover your WLAN
    Honeypots
Use measures for preventing radio waves from leaving or entering the building
  Use a certain type of paint on the walls
Use a router to only allow approved MAC addresses to access your network

## Slide 69: Countermeasures for Wireless Attacks (2 of 3)
Consider using an authentication server to authenticate users
  Instead of relying on a wireless device
Consider using EAP
  Allows using different protocols that enhance security
Consider placing the AP in the demilitarized zone (DMZ)
  Use a firewall in front of the company’s internal network that filters out traffic from unauthorized IP addresses
If possible, upgrade to WPA2 or WPA3, and replace hardware that can’t be upgraded

## Slide 70: Countermeasures for Wireless Attacks (3 of 3)
Assign static IP addresses to wireless clients
  Instead of using DHCP
Disable WPS
  Removes the known WPS attack vectors
Change the default SSID and disable SSID broadcasts
  If you can’t disable SSID broadcasts, rename default SSID

## Slide 71: Self-Assessment
What are the different types of attacks that an enterprise faces today?
What are the threats and vulnerabilities associated with embedded and specialized devices and mobile devices?
Notes: Instructions:
Use the Self-Assessment question to encourage students to evaluate their progress or goals in the course, as well as determine how they might apply their learning or grow as an individual.

## Slide 72: Summary
Now that the lesson has ended, you should be able to:
  Explain wireless technology
  Describe wireless networking standards
  Describe the process of authentication
  Describe wardriving
  Describe wireless hacking and tools used by hackers and security professionals